## Slide 1: Vertical Handoff in Heterogeneous Wireless Networks
Submitted to: Dr. Yossuf Khazbak

## Slide 2: Team 1
  Muhammad Alaa
  Muhammad Ahmad Hesham
  Hossam Alaa
  Mahmoud Amr

## Slide 3: AGENDA
  Heterogeneous Wireless Networks (HWN)
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 4: Heterogeneous Wireless Networks (HWN)
  Heterogeneity of WN architectures important feature of next generation of WN
  Mobile devices equipped with multiple radio access technologies RATs.
  HWN is a hierarchal structure of Coexistent different RATs like 2.5G, 3G, 4G, 5G, Wi-Fi, etc.
Notes: For example, a wireless network that provides a service through a WLAN and is able to maintain the service when switching to a cellular network is called a wireless heterogeneous network.
Different RATs are not separated you can switch for example between 4G and Wi-Fi with a press of a button causing the phone to disconnect from the wifi and connect to the 4G

## Slide 5: Heterogeneous Wireless Networks (HWN)

## Slide 6: Heterogeneous Wireless Networks (HWN)

## Slide 7: Heterogeneous Wireless Networks (HWN)

## Slide 8: Heterogeneous Wireless Networks (HWN)

## Slide 9: Heterogeneous Wireless Networks (HWN)

## Slide 10: Heterogeneous Wireless Networks (HWN)

## Slide 11: Heterogeneous Wireless Networks (HWN)

## Slide 12: Heterogeneous Wireless Networks (HWN)
Mobility
Data Rates
high
medium
pedestrian
Stationary
Basic voice
Text
Graphics
Compressed video
HQ multimedia
1G
2G
2.5G
3G
4G
WiMAX
802.11g
802.11b
Cordless Phone
1990
2003
2010

## Slide 13: Heterogeneous Wireless Networks (HWN)
  RATs differ in (Network Coverage, Bandwidth, etc.).
  HWNs Integrate all these different RATs to roam seamlessly.
  Higher levels in HWN hierarchy have higher coverage but less bandwidth.
  HWN is an Always Best Connected (ABC) network.

## Slide 14: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 15: Vertical Handoff
  Handoff is when a Mobile Terminal (MT) changes its point of attachment from on access point (AP) to another of same or different RAT.

## Slide 16: Vertical Handoff
  Handoff Classifications:
    Horizontal handoff (Intra-Network handoff)
    Vertical handoff (Inter-Network handoff)
      Upward VHO
      Downward VHO
    Diagonal handoff

## Slide 17: Vertical Handoff
  Handoff Classifications:
Vertical Handoff
Horizontal Handoff

## Slide 18: Vertical Handoff
  Handoff Classifications:
  Horizontal handoff
    when an MT moves from one cell to another within the same RAT.
    Main reasons:
      Poor Signal Quality (RSS)
      Bandwidth
      Velocity of MT
Notes: RSS is received signal strength

## Slide 19: Vertical Handoff
  Handoff Classifications:
  Horizontal handoff
    Steps:
      Handoff Initiation.
      Channel Assignment.
      Connection Transfer / handoff execution.

## Slide 20: Vertical Handoff
  Handoff Classifications:
  Vertical handoff
    when an MT moves from one RAT to another e.g. from Wi-Fi cell to a GSM/UMTS cell.
    Upward VHO: from lower size cell of a RAT with higher BW to bigger size cell of different RAT with lower BW.
    Downward VHO: opposite of upward VHO.

## Slide 21: Vertical Handoff
  Handoff Classifications:
  Vertical handoff
Upward VHO
downward VHO
Satellite
GSM
WiMAX
Wi-Fi
Bluetooth

## Slide 22: Vertical Handoff
  Handoff Classifications:
  Diagonal handoff
    Combination of vertical and horizontal handoffs.
    Termed as Media Independent Handover (MIH) in IEEE 802.21

## Slide 23: Vertical Handoff
  Vertical Handoff Decision Criteria:
  Network Related Attributes
  User Related Attributes
  User Preferences

## Slide 24: Vertical Handoff
  Vertical Handoff Decision Criteria:
  Network Related Attributes
    Bandwidth
    Network coverage
    Usage cost, Delay
    Signal to Noise Ratio (SNR)
    Received Signal Strength (RSS)
    Signal to Interference Ratio (SIR), Carrier to Interference Ratio (CIR)

## Slide 25: Vertical Handoff
  Vertical Handoff Decision Criteria:
  Network Related Attributes
  User Related Attributes
  User Preferences

## Slide 26: Vertical Handoff
  Vertical Handoff Decision Criteria:
  User Related Attributes
    Remaining Battery Power.
    Speed of Mobile Terminal.
    Type of Service Requested.

## Slide 27: Vertical Handoff
  Vertical Handoff Decision Criteria:
  Network Related Attributes
  User Related Attributes
  User Preferences

## Slide 28: Vertical Handoff
  Vertical Handoff Decision Criteria:
  User Preferences
    User preferences are expressed in terms of relative user preference weights.

## Slide 29: Vertical Handoff
  Vertical Handoff Research Challenges:
  Seamless Handoff
  Timing
  Throughput
  Security
  Power consumption
  Quality of Service (QoS) & Quality of Experience (QoE)

## Slide 30: Vertical Handoff
  Vertical Handoff Research Challenges:
  Seamless Handoff
    Uninterrupted application execution during handoff.
  Timing
    when to handoff? To reduce No. of Handoffs, Ping pong effect and Handoff failure.

## Slide 31: Vertical Handoff
  Vertical Handoff Research Challenges:
  Throughput
    How to increase the throughput by reducing the handoff delay and packet loss?
  Security
    Handoff to a more secure network.

## Slide 32: Vertical Handoff
  Vertical Handoff Research Challenges:
  Power consumption
    Power consumption in mobile terminal has to be minimized in case of mobile controlled handoff approach.
  Quality of Service (QoS) & Quality of Experience (QoE)
    QoS is objective from the networks perspective.
    QoE is subjective from user’s perspective to assess service quality of a network.

## Slide 33: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 34: Vertical Handoff Management Process
  Consists of the following Phases
    Handoff information gathering.
    Network Selection / Handoff decision.
    Handoff execution.

## Slide 35: Vertical Handoff Management Process
  Consists of the following Phases
    Handoff information gathering.
      AKA System Discovery or Network Discovery.
      collects information about the various handoff decision parameters.

## Slide 36: Vertical Handoff Management Process
  Consists of the following Phases
    Network Selection / Handoff Decision.
      Decides when and Where to trigger the handoff by analyzing the information gathered in earlier phase.
      Classified as:
        RSS based, Bandwidth based
        Multi Attribute Decision Methods (MADM) using utility functions
        Combination algorithm based on Neural Network & Game Theory.

## Slide 37: Vertical Handoff Management Process
  Consists of the following Phases
    Handoff execution.
      Implementation Phase.
      Executes actual connection transition from RTA to another.

## Slide 38: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 39: Vertical Handoff Decision Techniques
  Naïve Methods:
    Limited number of attributes
    Less reliability
      Most Stable RSS (Received Signal Strength)
      Maximum BW (Bandwidth)
      Minimum Cost

## Slide 40: Vertical Handoff Decision Techniques
  Complex Methods:
    Large number of attributes (MADM)
    More reliability
    Neural Networks and Fuzzy Logic to estimate weights
      SAW
      MEW
      TOPSIS

## Slide 41: Vertical Handoff Decision Techniques
  SAW:
    Summative Additive Weighting
    Each parameter is given a weight and each parameter is normalized
: Network index | : Network that maximizes the utility
: Parameter index | : Weight of parameter
𝑚: Number of parameters | : Normalized value of parameter in network
𝑚: Number of parameters | 

## Slide 42: Vertical Handoff Decision Techniques
  MEW:
    Multiplicative Exponential Weighting
      : Network index
      : Parameter index
      : Number of parameters
      : Network that maximizes the utility
      : Weight of parameter
      : Normalized value of parameter in network

## Slide 43: Vertical Handoff Decision Techniques
  TOPSIS:
    Techniques for Order Preference by Similarity to Ideal Solution
      Estimates the Euclidean distance to the ideal case
      Estimates the Euclidean distance to the worst case
      Choose the closest network to the ideal case
    Most used technique

## Slide 44: Vertical Handoff Decision Techniques
  TOPSIS:
=
: Network index | : Network that maximizes the utility
: Parameter index | : Weight of parameter
𝑚: Number of parameters | : Normalized value of parameter in network
: | :
𝑚: Number of parameters | 

## Slide 45: Vertical Handoff Decision Techniques
  TOPSIS example:
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5

## Slide 46: Vertical Handoff Decision Techniques
  TOPSIS example:
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 |  | 
 | 0.4 |  | 
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 |  | 
 | 0.4 |  | 

## Slide 47: Vertical Handoff Decision Techniques
  TOPSIS example:
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 
 | 0.4 | 0.4 | 
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 
 | 0.4 | 0.4 | 

## Slide 48: Vertical Handoff Decision Techniques
  TOPSIS example:
= 0.08
= 0.4195
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
= = 0.16015

## Slide 49: Vertical Handoff Decision Techniques
  TOPSIS example:
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
= 0.4418
= 0
= = 1

## Slide 50: Vertical Handoff Decision Techniques
  TOPSIS example:
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
= 0.2343
= 0.24597
= = 0.4789

## Slide 51: Vertical Handoff Decision Techniques
  TOPSIS example:
= Network1
 | Coverage () | RSS () | Power ( 0.6)
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8
Network1 (4G) | 0.8 | 0.5 | 0.2
Network2 (WiFi) | 0.4 | 0.4 | 0.8
Network3 (WiMax) | 0.5 | 0.6 | 0.5
 | 0.8 | 0.6 | 0.2
 | 0.4 | 0.4 | 0.8

## Slide 52: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 53: Game Theory Introduction
What is game theory ?
  A useful analytical tool.
  Used to model situations where there are multiple decision makers.
  Decision makers’ actions might have mutual ,possibly conflicting, consequences.

## Slide 54: Game Theory Introduction
What is game theory ?
  Usually used in the field of economics.
  Ex : Decide Whether a company should enter a new market.
  The new market’s payoff depends on the decision made by the company’s competitors.

## Slide 55: Game Theory Introduction
Non-cooperative Games
  Players have conflicting interests.
  All players are rational.
  Aim to maximize their own payoffs or utilities.
Static games
  Also called a single-stage game.
  Each player has only one move as a strategy.

## Slide 56: Game Theory Introduction
Static game formulation G(P, S, U)
  A static game is composed of the following components
    P : A set of players or decision makers.
    S : A set of strategies/moves/actions for each player.
    Strategy profile s : Set of chosen strategies by each player s = {s1, s2, .. }
    U : A set of utility functions for each player.
    Maps a strategy profile to the payoff of a certain player.

## Slide 57: Game Theory Introduction
Static game example (Multiple access Game)
  Players
    Share the same communication channel.
    Want to transmit a single packet each to a different receiver.
    The players and receivers are in the same power range.
P1
P2

## Slide 58: Game Theory Introduction
Static game example (Multiple access Game)
  Strategy/moves/actions:
    Each player can do one of two actions:
      Access the channel (A)
      Wait (W)
P1
P2

## Slide 59: Game Theory Introduction
Static game example (Multiple access Game)
  Utility function/ payoff matrix
P1
P2
W
W
A
A
P2
P1
0, 0

## Slide 60: Game Theory Introduction
Static game example (Multiple access Game)
  Utility function/ payoff matrix
P1
P2
W
W
A
P2
P1
0, 0
1-C, 0
A

## Slide 61: Game Theory Introduction
Static game example (Multiple access Game)
  Utility function/ payoff matrix
P1
P2
W
W
A
P2
P1
0, 0
1-C, 0
0, 1-C
A

## Slide 62: Game Theory Introduction
Static game example (Multiple access Game)
  Utility function/ payoff matrix
P1
P2
W
W
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C
A

## Slide 63: Game Theory Introduction
Nash equilibrium (Game solution)
  Is a state where no player has any incentive to change its strategy.
  Every player has the strategy that maximizes its payoffs given the other players’ strategies.
  Is not necessarily the optimal solution.

## Slide 64: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: W, P2: W
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C

## Slide 65: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: W, P2: W
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C
No Equilibrium!

## Slide 66: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: W, P2: A
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C

## Slide 67: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: W, P2: A
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C

## Slide 68: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: W, P2: A
W
W
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C
Equilibrium !
A

## Slide 69: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: A, P2: A
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C

## Slide 70: Game Theory Introduction
Nash equilibrium (Game solution)
  P1: A, P2: A
W
W
A
A
P2
P1
0, 0
1-C, 0
0, 1-C
-C, -C
No Equilibrium !

## Slide 71: Game Theory Introduction
Nash equilibrium (Game solution)
  The Solution of the game by Nash equilibrium is either:
    Player 1 Access the channel & Player 2 waits.
    Player 1 waits & Player 2 Access the channel.
  In both cases no player takes any benefit if changes its strategy.

## Slide 72: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 73: Game Theory in Vertical Handoff
Game between Mobile users
  Mobile Users compete for joining a particular network.
  Each Mobile user aims to maximize its QoS.
  Formulation:
    Players : Mobile Users.
    Strategy : Each mobile user can either:
      Connect.
      No Change.
    Utilities : All mobile users aim to maximize their own QoS.
  Solution:
  A state where all mobile users have no incentive to change their decision.

## Slide 74: Game Theory in Vertical handoff
Game between Wireless Networks
  Wireless Networks compete for a particular Mobile user.
  Each Network aims to maximize the revenue of its service.
  Formulation:
    Players : Wireless Networks.
    Strategy : Each Wireless Network can either:
      Accept the user connection.
      Reject the user connection.
    Utilities : All Networks aim to maximize their own revenue.
  Solution:
  A state where all Networks have no incentive to change their decision.

## Slide 75: Game Theory in Vertical Handoff
Game between Mobile Users & Wireless Networks
  Mobile users and wireless networks mutually select each other.
  Both aim to maximize their own payoffs.
  Formulation:
    Players : U(All mobile users combined), N (All Networks combined).
    Strategy :
      Action for U {U1 connects to N1, U2 No change, ..etc}.
      Action for N {N1 accepts U1, N2 declines U3, … etc}.
    Utilities : Maximize revenue for all users and networks.
  Solution:
  A state where all Mobile users and networks have no intensive to change their strategies.

## Slide 76: AGENDA
  Heterogeneous Wireless Networks
  Vertical Handoff
  Vertical Handoff Management Process
  Vertical Handoff Decision Techniques
  Game Theory Introduction
  Game Theory in Vertical Handoff

## Slide 78: Useful Resources
  https://ieeexplore.ieee.org/document/8229862
  https://infoscience.epfl.ch/record/79715?ln=en
  https://www.investopedia.com/terms/n/nash-equilibrium.asp
  https://link.springer.com/chapter/10.1007/978-981-10-8240-5_47
  https://api.semanticscholar.org/CorpusID:16584343